## Slide 1
CAREWATCHER
Privacy-Preserving Ambient Healthcare Companion for Passive Wellness Monitoring
100% On-Device Ambient Health Intelligence with Zero Cloud Egress
First Interim Evaluation (Review 1) | Academic Year: 2026 – 2027
Department of Artificial Intelligence and Data Science
Project Guide
[Guide Name]
Assistant Professor
Department of AI & DS
Muthoot Institute of Technology and Science
Team Members (Group: [X])
Aaron (Roll No: [Roll No.])
[Member 2] (Roll No: [Roll No.])
[Member 3] (Roll No: [Roll No.])
[Member 4] (Roll No: [Roll No.])
CareWatcher, Dept of AI and DS
1

## Slide 2
GERIATRIC HEALTHCARE & AMBIENT MONITORING
Problem Statement
1. Solitary Living & Silent Decline
• Surging Demographic: 1 in 6 people globally will be aged 60+ by 2030, with a vast majority living independently.
• Medication Non-Adherence: Over 50% of elderly with chronic conditions forget or mismanage prescribed dosages.
• Silent Deterioration: Subtle mood shifts, sleep degradation, and reduced mobility go unnoticed until an acute crisis occurs.
• Delayed Distress Response: Physical falls or acute medical distress often result in prolonged immobilization before help arrives.
2. The Cloud Privacy Dilemma
• Invasive Egress: Commercial assistants (Alexa, Google Home, smart cams) continuously stream raw domestic audio and video to third-party cloud servers.
• Resident Rejection: Elderly individuals strongly reject camera surveillance in private bedrooms and living quarters due to dignity loss.
• Regulatory & Security Risk: Transmission and cloud storage of sensitive biometric data violates strict healthcare privacy standards (HIPAA, GDPR).
• Recurring Costs: Cloud health monitoring services impose mandatory monthly subscription fees that strain low-income seniors.
3. Technical & Algorithmic Limits
• Internet Single Point of Failure: Broadband or router outages render cloud-dependent emergency detection totally offline.
• LLM Hallucination Threat: Unconstrained generative LLMs risk inventing dangerous medical diagnoses or clinical directives.
• Alarm Fatigue: Generic threshold sensors bombard caregivers with false alarms, causing notification blindness.
• Lack of Auditability: Cloud-based AI decisions lack cryptographic provenance; no verifiable record exists if an alert is dropped.
CareWatcher, Dept of AI and DS
2

## Slide 3
CORE RESEARCH & ENGINEERING GOALS
Project Objectives
Objective 1: Hardware-Enforced Zero-Cloud Privacy Architecture
To design and engineer an ambient edge computing architecture featuring a physical Privacy Shutter hard gate, ensuring 100% local on-device processing with mathematically verifiable zero network data egress.
▸ Physical gating of acoustic and visual sensors (guaranteed 0 bytes passed when shutter is closed).
▸ Full local execution of speech recognition, natural language reasoning, and database storage without cloud APIs.
Objective 2: Multimodal Passive Ambient Sensing & Trend Analysis
To integrate contactless acoustic speech, local quantized LLMs, and an ESP32 multi-biosensor telemetry hub (MAX30102 PPG, MLX90614 IR Temp, MPU-6050 Motion) to passively monitor medication adherence and detect vital drift.
▸ Schema-constrained JSON extraction from natural resident voice responses during conversational check-ins.
▸ Statistical rolling baseline trend engine with Z-score drift alerts (flagging abnormal heart rate, SpO2, sleep, or mood changes).
Objective 3: Decoupled Proposer-Verifier Safety & Audit Provenance
To construct an isolated dual-engine safety pipeline with an append-only, SHA-256 hash-chained cryptographic audit log to eliminate diagnostic hallucinations and provide tamper-proof accountability.
▸ Independent Safety Verifier enforces strict clinical deny-lists, tone validation, and anti-fatigue rate limiting.
▸ Immutable, hash-chained ledger storing every sensory reading, proposal, and verification decision with 100% replay integrity.
CareWatcher, Dept of AI and DS
3

## Slide 4
CONCISE SUMMARY & SYSTEM RATIONALE
Project Overview
ENGINEERING PROBLEM
Real-Time Edge AI under Resource Constraints
Executing concurrent wake-word detection, speech-to-text (Whisper), LLM conversational reasoning, and continuous biosensor telemetry on consumer edge hardware with <8s latency, zero cloud offloading, and deterministic memory consumption.
MOTIVATION
Dignified Autonomy for Vulnerable Seniors
Enabling aging individuals to live independently without feeling under surveillance. Replacing intrusive cameras with ambient conversational check-ins and passive non-contact vital sensing.
NEED FOR PROJECT
The Global Geriatric Caregiving Crisis
Acute shortage of professional geriatric aides combined with rising elderly populations living alone. Existing smart assistants violate privacy; CareWatcher delivers continuous safety without data leakage.
TARGET USERS
Elderly Individuals & Healthcare Stakeholders
Primary: Solitary elderly residents, mobility-limited individuals, post-operative recovering patients. Secondary: Family caregivers, geriatric nurses, assisted living facility administrators.
SCOPE OF PROJECT
Ambient Wellness Monitoring (Non-Clinical)
Covers conversational medication checks, rolling vital drift detection (BPM, SpO2, Temperature), immobility/fall alerts, and encrypted audit logging. Explicitly excludes clinical diagnosis and invasive wearable mandates.
EXPECTED IMPACT
Safe, Resilient & Cost-Free Ambient Care
100% privacy preservation (HIPAA/GDPR compliant by design), zero recurring cloud subscription fees, resilient offline operation during network blackouts, and prompt caregiver alerting.
CareWatcher, Dept of AI and DS
4

## Slide 5
MILESTONES, IMPLEMENTATION STATUS & FEEDBACK INCORPORATION
Progress Since Zeroth Review
Parameters | Zeroth Review Proposal | Current Status (Review 1)
Literature Survey | Reviewed 15+ broad papers on smart home IoT and ambient assisted living. | Completed survey on Edge AI, Faster-Whisper, quantized LLMs, and non-clinical safety verification.
Problem Definition | General concept of smart elderly assistant with cloud sync. | Refined to 100% on-device, privacy-preserving companion with strictly non-clinical boundaries.
Architecture | Initial high-level block diagram with shared modules. | Engineered modular 8-stage pipeline with hard Privacy Shutter and isolated Proposer ↔ Verifier.
Algorithms | Planned simple rule-based keyword matching. | Implemented Faster-Whisper STT, Mistral-7B schema JSON extraction, and Z-score rolling drift algorithms.
Hardware | Preliminary sensor list (conceptual selection). | Built ESP32 sensor hub (MAX30102 PPG, MLX90614 IR Temp, MPU-6050) + local mic/webcam drivers.
Software | No codebase or implementation. | Engineered complete modular Python 3.11 core (82/82 passing tests) + Local Web Dashboard.
COMMITTEE SUGGESTIONS INCORPORATED
• Committee Suggestion 1: Prevent generative AI from offering unverified clinical diagnoses or prescribing medications. ➔ Action Taken: Created a fully decoupled SafetyVerifier that checks every proposed intervention against a strict medical deny-list, non-clinical language guidelines, and anti-fatigue rate limits before audio delivery.
• Committee Suggestion 2: Provide tangible architectural proof that user privacy is strictly guaranteed without trusting external servers. ➔ Action Taken: Implemented a software/hardware-gated PrivacyShutter with automated fuzz verification confirming 0 bytes pass downstream when shutter is CLOSED, alongside zero cloud egress.
CareWatcher, Dept of AI and DS
5

## Slide 6
DECOUPLED 5-LAYER EDGE PIPELINE WITH ROOT OF PRIVACY
System Requirements & Architecture Design
Layer 1: Perception
Hardware & Sensors
• Mic Source 16kHz local audio stream
• Webcam Pres. Local OpenCV Haar cascade; NO video/frames saved
• ESP32 Sensor Hub MAX30102 (BPM & SpO2 via I2C)
• MLX90614 Contactless IR forehead temp
• MPU-6050 6-axis motion & fall accelerometer
Layer 2: Privacy Root
Physical Shutter Gate
• Privacy Shutter Hard gate root boundary
• Binary State CLOSED (default) / OPEN
• Hard Isolation Zero bytes flow downstream when closed
• Manual/Voice Hardware switch & voice command toggling
• Fuzz Validated 100% leak-proof verification
Layer 3: Cognition
Edge AI Pipeline
• Wake Word 'hey care' keyword detector
• Whisper STT Local Faster-Whisper base model
• Mistral-7B 4-bit GGUF via llama.cpp on CPU
• Schema Guard Enforced JSON HealthEvent dataclass
• Zero Cloud Zero external network calls
Layer 4: Memory & Drift
Trends & Storage
• Resident DB Local SQLite3 encrypted store
• Rolling Baseline 7-day sliding window vitals
• Drift Engine Z-score statistical deviation
• Vital Drift SpO2 <92%, BPM delta >20
• Inactivity Check 90-min sedentary threshold
Layer 5: Safety & Action
Verifier & Delivery
• Rule Proposer Generates candidate interventions
• Safety Verifier Independent gate (no imports of Proposer)
• Medical Deny-List Blocks diagnostic/clinical terms
• Piper TTS Local neural speech delivery
• SHA-256 Audit Tamper-evident hash-chained log
CareWatcher, Dept of AI and DS
6

## Slide 7
END-TO-END MULTIMODAL PROCESSING WORKFLOW
Methodology & Execution Pipeline
AI & Conversational Intelligence Methodology
• Speech Processing Pipeline: Captures 16 kHz raw PCM audio chunks. Ingests via Faster-Whisper base model (CTranslate2 CPU backend) for fast word-error-rate performance without external speech APIs.
• Wake-Word Activation: Keyword detection pipeline continually scans transcripts for 'hey care' before triggering active conversational agent state.
• Schema-Constrained LLM Reasoning: Utilizes 4-bit quantized Mistral-7B-Instruct (Q4_K_M GGUF) via llama.cpp. Prompts strictly constrain output to validated JSON schemas (category, summary, confidence, mood_label).
• Rolling Baseline Drift Detection: Maintains 7-day personal vital statistics (mean, standard deviation). Detects anomalies via dynamic thresholds (e.g., SpO2 < 92%, BPM shift > 20, continuous negative sentiment).
• Verification Testing: Automated test suite (test_agent.py, test_pipeline.py) rigorously evaluates prompt adherence and schema validation against synthetic conversational transcripts.
Hardware Integration & Safety Verification Methodology
• Microcontroller Hub & Bus Architecture: ESP32-WROOM-32 coordinates MAX30102 (PPG) and MLX90614 (IR Temp) over I2C (GPIO 21 SDA, GPIO 22 SCL) and HC-SR501 over GPIO 13. Communicates via USB Virtual COM @ 115200 baud.
• Physical Shutter Gating: All incoming sensory feeds pass through the PrivacyShutter state machine. Gated at the root boundary: zero bytes exit driver layers when shutter is CLOSED.
• Decoupled Safety Verifier: Zero shared imports with Proposer engine. Inspects every proposed intervention for clinical claims, quiet hours (22:00–07:00), and rate-limits (max 3 reminders/hour).
• Actuation & Delivery: Approved interventions synthesize locally via Piper neural TTS (en_US-lessac voice) and stream real-time JSON events to the local Web Dashboard.
• Tamper-Evident SHA-256 Audit: Each event (readings, proposals, verifier decisions) is hashed deterministically with the previous block's SHA-256 digest, guaranteeing cryptographic integrity.
CareWatcher, Dept of AI and DS
7

## Slide 8
CURATED SELECTION FOR PRIVACY, PERFORMANCE, AND EDGE INDEPENDENCE
Technology Stack & Technical Justifications
Stack Layer | Technology / Framework | Technical Justification & Architectural Trade-off
Microcontroller Hub | ESP32-WROOM-32 | Low-cost dual-core 240MHz SoC with hardware I2C/UART; supports real-time biosensor acquisition with zero OS jitter.
PPG Biosensor | MAX30102 Pulse Oximeter | Dual-wavelength (660nm & 880nm) photoplethysmography providing clinical-grade heart rate and SpO2 readings.
IR Temperature | MLX90614 Contactless IR | Medical-grade non-contact thermometry (±0.2°C accuracy); measures body temperature passively without touching the resident.
Motion & IMU | MPU-6050 6-Axis Accelerometer | Detects resident tremors, room movement, and sudden high-g impact forces characteristic of physical falls.
Speech-to-Text | OpenAI Faster-Whisper (base) | CTranslate2 optimized; 4x faster execution & 50% less RAM than vanilla Whisper, enabling low-latency CPU speech transcription.
Edge LLM Reasoning | Mistral-7B Q4_K_M (llama.cpp) | Quantized 4-bit weights run within 4GB RAM on standard laptop CPU; provides structured JSON health event extraction.
Neural Speech Synth | Piper TTS / pyttsx3 | High-fidelity, ultra-low latency neural text-to-speech engine running 100% locally with zero cloud streaming.
Local Database | SQLite 3 (data/resident.db) | Zero-configuration, ACID compliant serverless SQL engine; maintains rolling resident baselines and event history locally.
Web Architecture | Python http.server + Vanilla JS | Standard library HTTP server with zero third-party web bloat; renders real-time dashboard UI directly on localhost.
CareWatcher, Dept of AI and DS
8

## Slide 9
EMPIRICAL EVIDENCE OF WORKING SYSTEM IMPLEMENTATION
Preliminary & Interim Results
Live Operational Web Dashboard (Running on Localhost)
Fig 9.1: CareWatcher live web UI displaying active Privacy Shutter, real-time ESP32 vitals telemetry, conversational audit trail, and zero-cloud shield verification.
Validated Functional Milestones (M0 to M8 Complete)
✔ Automated Test Suite: 82 / 82 tests passing (100% pass rate in 3.03s) across config, shutter, STT, LLM schema parsing, memory store, and audit logging.
✔ Privacy Shutter Verification: Automated fuzz tests confirm 0 bytes leaked when shutter is in CLOSED state. Physical toggle verified in live runtime.
✔ Conversational Extraction: Resident voice utterance 'hey care I forgot to take my morning blood pressure pills' accurately transcribed and parsed into structured MEDICATION event.
✔ Rolling Baseline Drift Detection: Injected 110 BPM tachycardia reading immediately triggered drift alert against resident's 72 BPM baseline (Z-score > threshold).
✔ Safety Verifier Efficacy: 100% rejection rate for diagnostic/prescriptive medical words in deny-list; strictly enforced non-clinical reminder phrasing.
✔ Cryptographic Audit Chain: Deterministic SHA-256 hashing verified with 100% valid blockchain-style sequence integrity across all system events.
CareWatcher, Dept of AI and DS
9

## Slide 10
QUANTIFIED PROGRESS BREAKDOWN (70% COMPLETED | 30% REMAINING)
Remaining Work & Completion Status
PROJECT STATUS: 70% COMPLETED (CORE PIPELINE OPERATIONAL) | 30% REMAINING (PHYSICAL HOUSING & FIELD PILOT)
1. Physical Enclosure & Hardware Packaging
Current: 40% Complete | Target: W16
• CAD modeling of the desktop companion enclosure. • 3D printing of durable housing with integrated physical sliding shutter. • PCB perf-board assembly connecting ESP32, MAX30102, and status LEDs.
2. Extended Residential Field Pilot Trial
Current: 30% Complete | Target: W17
• Deploying prototype in a 7-day residential test with elderly participant. • Calibrating personal baseline parameters across real-world sleep and activity. • Collecting usability feedback regarding voice clarity and prompt naturalness.
3. Edge Hardware Acceleration & Optimization
Current: 60% Complete | Target: W18
• Exploring INT4 NPU / Vulkan GPU offloading to reduce LLM latency (<1.5s). • Fine-tuning wake-word detector sensitivity to minimize false rejections. • Optimizing ESP32 low-power deep sleep cycles during inactive hours.
4. Comprehensive Thesis & Academic Paper
Current: 45% Complete | Target: W19
• Finalizing B.Tech comprehensive project report and operational manual. • Documenting security audit verification and clinical safety deny-list rules. • Submitting research paper: 'Decentralized Ambient Healthcare Companion via On-Device LLMs and Physical Privacy Gating'.
CareWatcher, Dept of AI and DS
10

## Slide 11
20-WEEK MAJOR PROJECT DEVELOPMENT ROADMAP
Updated Project Timelines & Gantt Schedule
Project Phase & Activity | Timeline (Weeks) | Key Milestones & Deliverables | Status
Phase 1: Survey & Formal Specification | Weeks 1 – 3 | Literature survey, SPEC.md, interfaces definition | COMPLETED
Phase 2: Privacy Shutter & Sensor Drivers | Weeks 4 – 6 | Privacy shutter gate, mic driver, ESP32 firmware | COMPLETED
Phase 3: STT & LLM Conversation Agent | Weeks 7 – 9 | Faster-Whisper integration, Mistral schema parsing | COMPLETED
Phase 4: Trend Engine, Proposer & Verifier | Weeks 10 – 12 | Rolling drift Z-scores, SafetyVerifier, SHA-256 audit | COMPLETED
Phase 5: Local Dashboard & Integration | Weeks 13 – 14 | Web UI, HTTP API server, 82 unit tests [REVIEW 1] | COMPLETED
Phase 6: 3D Packaging & Enclosure Fabrication | Weeks 15 – 16 | CAD housing design, 3D printing, physical slider switch | IN PROGRESS
Phase 7: Residential Pilot & Edge Optimization | Weeks 17 – 18 | 7-day elderly trial, INT4 acceleration [REVIEW 2] | PENDING
Phase 8: Final Thesis & Defense Demonstration | Weeks 19 – 20 | Comprehensive report, conference paper, final viva | PENDING
CareWatcher, Dept of AI and DS
11

## Slide 12
ACADEMIC LITERATURE, BIOMEDICAL STANDARDS & CORE FRAMEWORKS
References
[1] A. Radford, J. W. Kim, T. Xu, G. Brockman, C. McLeavey, and I. Sutskever, 'Robust Speech Recognition via Large-Scale Weak Supervision,' OpenAI Technical Report, 2022.
[2] H. Touvron, L. Martin, K. Stone, P. Albert, et al., 'LLaMA: Open and Efficient Foundation Language Models,' arXiv:2302.13971, 2023.
[3] P. Rashidi and A. Mihailidis, 'A Survey on Ambient-Assisted Living Tools for Older Adults,' IEEE Transactions on Biomedical Engineering, vol. 60, no. 3, pp. 679-688, 2013.
[4] T. Tamura, Y. Maeda, M. Sekine, and M. Yoshida, 'Wearable Photoplethysmographic Sensors—Past and Present,' Electronics, vol. 3, no. 2, pp. 282-302, 2014.
[5] S. Gerke, T. Minssen, and G. Cohen, 'Ethical and Legal Challenges of Artificial Intelligence-Driven Healthcare,' Artificial Intelligence in Healthcare, pp. 295-336, Academic Press, 2020.
[6] S. Haber and W. S. Stornetta, 'How to Time-Stamp a Digital Document,' Journal of Cryptology, vol. 3, no. 2, pp. 99-111, 1991.
[7] C. Dwork and A. Roth, 'The Algorithmic Foundations of Differential Privacy,' Foundations and Trends in Theoretical Computer Science, vol. 9, no. 3-4, pp. 211-407, 2014.
[8] World Health Organization, 'Regulatory Considerations on Artificial Intelligence for Health,' WHO Health Guidance Document, Geneva, 2023.
[9] ISO/IEEE 11073-10408:2020, 'Health Informatics—Personal Health Device Communication—Device Specialization: Thermometer,' IEEE Standards Association, 2020.
[10] ISO/IEEE 11073-10404:2020, 'Health Informatics—Personal Health Device Communication—Device Specialization: Pulse Oximeter,' IEEE Standards Association, 2020.
[11] A. Q. Jiang, A. Sablayrolles, A. Mensch, C. Bamford, et al., 'Mistral 7B,' arXiv:2310.06825, 2023.
[12] J. Varghese, D. A. Joseph, and R. Paul, 'Edge Computing in Ambient Assisted Living: Architectures, Challenges, and Privacy Guarantees,' IEEE Access, vol. 9, pp. 78622-78652, 2021.
CareWatcher, Dept of AI and DS
12